## Slide 1
Acoustic Detection of Room Shape
Joshua Morgan, Anish Phule, Zaiyue Lu

## Slide 2
Objective
Detect the positions of walls by measuring sound of a speaker reflected by the walls at multiple locations of microphones
Measure the sound of a speaker reflected by walls at multiple locations of microphone
Implement algorithm in MATLAB to determine the positions of walls by analyzing the measured sound wave

## Slide 3
Applications
Acoustic Virtual Reality
Audio Forensics
Indoor Positioning
Architectural Acoustics

## Slide 4
Relevant Works
Discuss various methods for obtaining the room impulse function
Adrian Calin Farcas, and Marina Dana Topa, “On the choice of the method for obtaining the room impulse response”, Acta Technica Napocensis 54, 34 (2003)
Stan Guy-Bart, Embrechts Jean-Jacques, and Archambeau Dominique, “Comparison of different impulse response measurement techniques”, Journal of the Audio Engineering Society 50, 249-262 (2002)
Angelo Farina, “Simultaneous Measurement of Impulse Response and Distortion With a Swept-Sine Technique”, 108th Convention, Audio Engineering Society, February 19-22, 2000, Paris, France
Reconstruct the 3D geometry of a room
I. Dokmanic, R. Parhizkar, A. Walther, Y. Lu, and M. Vetterli, “Acoustic echoes reveal room shape”, Proceedings of the National Academy of Sciences of the United States of America 110, 12186-12191 (2013)
Introduce strategy to detect position of walls with 20 cm uncertainty in microphone positions, and absorption coefficient of sound
Oliver Shih, and Anthony Rowe, “Can a Phone Hear the Shape of a Room?”, IPSN ’19: Proceedings of the 18th International Conference on Information Processing in Sensor Networks, Pages 277-288, April 16-18, 2019, Montreal, Canada

## Slide 5
Image Source Model of Room Shape

## Slide 6: Each reflection is equivalent to a direct path from an image source

## Slide 7: Each reflection is equivalent to a direct path from an image source
Source
Image Source

## Slide 8: First order image sources correspond to single reflections
Source

## Slide 9: First order image sources correspond to single reflections
Source
Image Source
(first order)

## Slide 10: Higher order image sources correspond to multiple reflections
Source

## Slide 11: Higher order image sources correspond to multiple reflections
Source
Image Source (second order)

## Slide 12: Each first order image source corresponds to a wall
Source ()
Image Source ()
A wall is defined by the linear constraint

## Slide 13: Each first order image source corresponds to a wall
Source ()
Image Source ()
Inside room:
Outside room:

## Slide 14: A room is the intersection of wall constraints

## Slide 15
Room Shape Estimation Algorithm

## Slide 16: The room estimation algorithm determines first order image source locations from received signals
Transmitted Signal
Received Signals
Impulse Response Estimation
Speaker and Image Source Localization
Remove Incorrect Image Sources
Cuboid Fit
Echo Time-of-Flights
Candidate Image Sources
First Order Image Sources
Room Dimensions

## Slide 17: The room estimation algorithm determines first order image source locations from received signals
Transmitted Signal
Received Signals
Impulse Response Estimation
Speaker and Image Source Localization
Remove Incorrect Image Sources
Cuboid Fit
Echo Time-of-Flights
Candidate Image Sources
First Order Image Sources
Room Dimensions

## Slide 18: A single speaker and multiple microphones are placed in the room

## Slide 19: Each microphone has its own impulse response
Transmitted Signal
Received Signal
Room Impulse Response
Inverse filter, for recovery of impulse response:

## Slide 20: The transmitted signal is a sine sweep covering a frequency range of 5 Hz to 22.05 kHz

## Slide 21: In simulation, the inverse filter effectively recovers the room impulse response

## Slide 22: Echo times are extracted from the room impulse responses
First peak corresponds to direct path

## Slide 23: The room estimation algorithm determines first order image source locations from received signals
Transmitted Signal
Received Signals
Impulse Response Estimation
Speaker and Image Source Localization
Remove Incorrect Image Sources
Cuboid Fit
Echo Time-of-Flights
Candidate Image Sources
First Order Image Sources
Room Dimensions

## Slide 24: Each time-of-flight defines a spherical constraint, and the image source can be found using the intersection of constraints
X (m)
Y (m)
Z (m)
: estimated image source location

## Slide 25: Each image source location is derived from a nonlinear least squares fit
Microphone coordinates:
Measured time-of-flight at :
Estimated image source location:

## Slide 26: If microphones are placed on a 2D plane, the image source fit has multiple solutions
Top View:
Bottom View:

## Slide 27: It is difficult to determine corresponding echo measurements between each impulse response

## Slide 28: It is difficult to determine corresponding echo measurements between each impulse response
Use first peak as direct path for speaker localization

## Slide 29: It is difficult to determine corresponding echo measurements between each impulse response
Do these echoes come from the same image source?

## Slide 30: It is difficult to determine corresponding echo measurements between each impulse response
Do these echoes come from the same image source?

## Slide 31: It is difficult to determine corresponding echo measurements between each impulse response
Do these echoes come from the same image source?

## Slide 32: Source localization is attempted at each possible combination of echoes
For T microphones, and using the first M peaks, we get candidate image sources
Score for candidate image source :
Discard all candidates with
We use cm for simulation, cm for experimental data

## Slide 33: The computational burden is greatly reduced by the intermicrophone distance criteria
Do not attempt matching echoes which are farther apart than the distance between microphones
This constraint is more useful if microphones are placed close together, and farther away from the room center

## Slide 34: The room estimation algorithm determines first order image source locations from received signals
Transmitted Signal
Received Signals
Impulse Response Estimation
Speaker and Image Source Localization
Remove Incorrect Image Sources
Cuboid Fit
Echo Time-of-Flights
Candidate Image Sources
First Order Image Sources
Room Dimensions

## Slide 35: The set of candidate image sources contains higher order sources

## Slide 36: Higher order sources are represented as combinations of lower order sources
Source
(second order)
(first order)
(first order)

## Slide 37: Higher order sources are represented as combinations of lower order sources
Source
(second order)
(first order)
(first order)

## Slide 38: Higher order sources are represented as combinations of lower order sources
Source
(second order)
(first order)
(first order)

## Slide 39: Higher order sources are represented as combinations of lower order sources
Source
(second order)
(first order)
(first order)

## Slide 40: Higher order sources are represented as combinations of lower order sources
Source
(second order)
(first order)
(first order)

## Slide 41: Higher order sources are represented as combinations of lower order sources
Source
(second order)
(first order)
(first order)

## Slide 42: Higher order sources are represented as combinations of lower order sources
Source
(second order)
(first order)
(first order)
+

## Slide 43: Higher order sources are identified and removed using the combination test

## Slide 44: The room estimation algorithm determines first order image source locations from received signals
Transmitted Signal
Received Signals
Impulse Response Estimation
Speaker and Image Source Localization
Remove Incorrect Image Sources
Cuboid Fit
Echo Time-of-Flights
Candidate Image Sources
First Order Image Sources
Room Dimensions

## Slide 45: The final list of first order image sources has false positives which distort the estimated room shape
The groundtruth room is an (8 m)x(8 m)x(3 m) cuboid

## Slide 46: A point cloud cuboid fitting algorithm produces the final room shape estimate

## Slide 47
Simulation Results

## Slide 48: In simulation, the room shape is successfully extracted

## Slide 49: Performance degrades as the microphone array moves farther from the center
Failed shape extraction

## Slide 50
Experimental Setup

## Slide 51
Experimental Setup
Requirements:
Need to setup Microphone and Speaker to get the reflection data
Need a specific signal to be played
The microphone and speaker need to work synchronously to have minimum lag

## Slide 52
Experimental Setup(Software)
MATLAB function : AudioPlayerRecorder
Simultaneously plays and records via an audio device
Plays audio samples to and records audio samples from an audio device in real time.
Only Issue: The device recording and playing the audio must be the same.
Solution: Audio interface.

## Slide 53
Experimental Setup(Software)
Audio Signal:
Sweep tone function.
Exponential swept sine signal for t seconds, followed by silence of ts seconds.

## Slide 54
Experimental Setup(Hardware)
Audio
Interface

## Slide 55
Experimental Setup(Hardware)
Audio
Interface

## Slide 56
Experimental Setup(Hardware)
Audio
Interface

## Slide 57
Experimental Setup(Hardware)
Audio
Interface

## Slide 58
Actual Experiments

## Slide 59
Actual Experiments
Microphones with no height variation

## Slide 60
Actual Experiments
Microphones with no height variation

## Slide 61
Actual Experiments
Microphones with no height variation
Latency between speaker and microphone​

## Slide 62
Actual Experiments
Microphones with no height variation
Room Reconstruction

## Slide 63
Actual Experiments
Microphones with height variation

## Slide 64
Actual Experiments
Microphones with height variation
Room Reconstruction

## Slide 65
Actual Experiments
Room Size variation(Oven)

## Slide 66
Actual Experiments
Room Size variation(Oven)
Room Reconstruction

## Slide 67
Actual Experiments
Possible Explanation of results:
1. Microphones with no height variation:
The simulations assume the presence of an omni-directional speaker and concrete walls. The usage of a directional speaker and walls of different and thinner materials would mean different signals received and sound signals passing through(instead of reflecting), leading to a bad room reconstruction.
2. Microphones with height variation:
We see a huge number of image sources. This can be possibly due to the reflections from the bins used for increasing the height of the speaker and the microphone.
3. Room Size variation(Oven):
The grills in the oven are a very strange structure for the simulation, and the reflections can be the cause for the disturbance in the results, leading to a failure in the reconstruction.

## Slide 68
Summary
The goal was to measure the sound of a speaker reflected by walls at multiple locations of a microphone and reconstruct the room shape from that.
The project was motivated by applications in architectural acoustics and indoor positioning.
Simulated the experiment in MATLAB to estimate the size of an empty cuboidal room with various positions of the microphone to get satisfactory results.
Conducted experiments in various environments with varying constraints to observe the results and hypothesize the causes behind the same.

## Slide 69
Thank You! Questions?